## Slide 1: Introduction to Block Codes, Type of Block Codes
Prepared by
Prof. Hitesh Dholakiya
Modified by
Rifat Rahman
Assistant Professor
Institute of Appropriate Technology, BUET

## Slide 2: Block Code
Outlines
Basics of Channel and Codeword
Basic Structure of Communication Systems
Basics of Block Code
Important Parameters of Block Code
(4, 3) Block Code {Parity Check}

## Slide 3: Basics of Channel and Codeword
Channel
In communication systems, the channel is the medium through which the signal travels from the transmitter to the receiver.
  Examples: air (for wireless), cables, optical fiber, etc.
  Channels may introduce noise, interference, and distortion, causing errors in transmission.
Codeword
In digital communication, Information is transmitted as Codewords — specific binary sequences that represent data after encoding.
  Example: If message bits are m = 101, the encoder may convert it to a codeword c =
101110.
  Each codeword follows certain rules designed to detect or correct errors caused by the channel.

## Slide 4: Basic Structure of Communication Systems
Information
Transmitter
Channel
Noise
Receiver
Information
Transmitter
Source
Encoder
Channel
Encoder
Modulator
Receiver
Demodulator
Channel
Decoder
Source
Decoder
Source Encoding
To remove redundancy from the original message so it can be represented using fewer bits — i.e., to
compress the data efficiently.
  Text compression: Huffman coding, Arithmetic coding
  Image/video compression: JPEG, MPEG
Channel Encoding
To add redundancy to the transmitted data to make it robust to noise and errors in the communication channel.
  Examples: Linear Block Code (Hamming Code), Convolution Codes, Turbo Codes etc.
Source Encoding makes data smaller, and Channel Encoding makes data Stronger.

## Slide 5: Basics of Block Code
A Block Code is represented by (n, k) Block Code.
  n = Number of Bits in codeword
  k = Number of bits in Information
  r = n-k = Parity bits or Redundant bits
Information I = [i1, i2, i3, …… , ik]
Parity P = [P1, P2, P3, …… , Pr]
Codeword C = [i1, i2, i3, …… , ik, P1, P2, P3, …… , Pr]
Systematic codes
Systematic codes place message bits at the beginning of the codeword, followed by check bits, making the original message easily identifiable.
Non-Systematic codes
Non-systematic codes intersperse message and check bits, so the original message bits are not located at a fixed position.

## Slide 6: Parameters of Block Code (n, k)

## Slide 7: Block Code (4, 3)
Information bits (k = 3 bits) |  |  | Parity bit
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
Even Parity Check

## Slide 8: Block Code for Parity Check
Outlines
Basics of Block Code for Parity Check
Example of Block Code for Parity Check for Encoding
Decoding of Block Code for Parity Check
Example of Block Code for Parity Check for Decoding

## Slide 9: Basics of Block Code for Parity Check
Block Code for Parity Check is the simplest form of Error Control used for Error Detection.
Block Code for Parity Check can not Correct Error, it can only detect one-bit Error.
A parity bit is an additional bit added to make the number of 1’s in the codeword even
(even parity) or odd (odd parity).
  Even parity: Total number of 1’s is even.
  Odd parity: Total number of 1’s is odd.
In (n, k) Block Code for Parity Check, n = k+1, means we add one bit of parity (Even or Odd).
Information I = [i1, i2, i3, …… , ik]
For Even Parity bit P, P = i1 + i2 + i3 + ……… + ik {This sum is Mod 2 sum or XOR}
For Odd Parity bit P, P = i1 + i2 + i3 + ……… + ik + 1 {This sum is Mod 2 sum or XOR}
Codeword C = [i1, i2, i3, …… , ik, P]

## Slide 10: Example of Block Code for Parity Check with Encoding
Example 1: Given the (5, 4) Even Parity Block Code, find codewords corresponding to the Information I = [1 0 1 1] and [1 0 1 0]
  (5, 4) = (n, k)
  Information bits k = 4
  Parity Bits r = n – k = 5 – 4 = 1
  For Even Parity P = i1 + i2 + i3 + i4 {Sum means XOR Operation}
  Case I: P = 1 + 0 + 1 + 1 = 1
  So, Codeword C = [i1, i2, i3, i4, P] = [1, 0, 1, 1, 1]
  Case II: P = 1 + 0 + 1 + 0 = 0
  So, Codeword C = [i1, i2, i3, i4, P] = [1, 0, 1, 0, 0]

## Slide 11: Decoding of Block Code for Parity Check
At the Receiver stage, we receive n bits codeword V along with the Error.
V = [V1, V2, V3, …… , Vn]
To determine whether Received Codeword V is a correct codeword, we check the Mod 2
Sum of V.
V = V1 + V2 + V3 + ……… + Vn {This sum is Mod 2 sum or XOR}
For Even Parity Check, V should be 0; otherwise, there is an error in the received codeword.
For Odd Parity Check, V should be 1; otherwise, there is an error in the received codeword.

## Slide 12: Example of Block Code for Parity Check with Decoding
Example 1: Given the (8, 7) Even Parity Block Code, determine whether V1 = [10110110] and V2 = [01101001] give parity failures.
  (8, 7) = (n, k)
  Information bits k = 7
  Parity Bits r = n – k = 8 – 7 = 1
  P = V1 + V2 + V3 + V4 + V5 + V6 + V7 + V8 {Sum means XOR Operation}
  Case I: P = 1 + 0 + 1 + 1 + 0 + 1 + 1 + 0 = 1
  For Even Parity P = 0, but here we have Parity Failure, so the received codeword is incorrect.
  Case II: P = 0 + 1 + 1 + 0 + 1 + 0 + 0 + 1 = 0
  For Even Parity P = 0, so the received codeword is correct.

## Slide 13: Block Code for Product Code
Basics of Block Code for Product Code
A block code with a parity check cannot correct errors; it is only used to detect errors.
A block code using a product code can both detect and correct errors.
In block code for Product code, two parity-check matrices are combined to form a two- dimensional code structure that allows for both error detection and correction.

## Slide 14: Example of Block Code for Product Code Example 1: Given the Information I = [1 1 0 1 0 1 1 0 1 0 0 0 0 0 0 0 1 1 1 0 1 0 0 1], Structure the Block Code for Product Code (35, 24).
 | Data Bits |  |  |  | Row Parity | 
 | 1 | 1 | 0 | 1 | 1 | 
 | 0 | 1 | 1 | 0 | 0 | 
 | 1 | 0 | 0 | 0 | 1 | 
 | 0 | 0 | 0 | 0 | 0 | 
 | 1 | 1 | 1 | 0 | 1 | 
 | 1 | 0 | 0 | 1 | 0 | 
Column Parity | 0 | 1 | 0 | 0 | 1 | Overall Parity
Total 7 rows and 5 columns, so n = 35
Information bits, k = 24 bits
So, given block code is (35,24)
It is happening as per (5,4) x (7,6) = (35,24)
It is used to detect and correct a one-bit error.

## Slide 15: Block Code for Repetition Code
Basics of Block Code for Repetition Code
These are codes that repeat the information bits two or more times.
They are a type of block code denoted by (n, 1), where each message bit is encoded into an n-bit codeword.
  Example: (4, 1) = (n, k)
  n=4 and k=1
  Redundancy r = n - k = 4 - 1 = 3
Here, redundancy is not based on even or odd parity.

## Slide 16: Example of Block Code for Repetition Code
Example 1: For (3, 1) Block Code, Explain the Encoding and Decoding Process.
(3, 1) = (n, k)
n = 3 and k=1
Redundancy r = n - k = 3 - 1 = 2
Encoding Process
Data | Redundancy |  | Codeword |  | 
0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1
Decoding Process
  Decoding is done based on Majority Votes.
Received Data |  |  | Error | Output Data |  |  | Info
0 | 0 | 0 | No | 0 | 0 | 0 | 0
0 | 0 | 1 | One-bit | 0 | 0 | 0 | 0
0 | 1 | 0 | One-bit | 0 | 0 | 0 | 0
0 | 1 | 1 | One-bit | 1 | 1 | 1 | 1
1 | 0 | 0 | One-bit | 0 | 0 | 0 | 0
1 | 0 | 1 | One-bit | 1 | 1 | 1 | 1
1 | 1 | 0 | One-bit | 1 | 1 | 1 | 1
1 | 1 | 1 | No | 1 | 1 | 1 | 1
Majority Vote for (V1, V2, V3) is taken as per Info I = V1V2 + V1V3 + V2V3